## Slide 1
LAB 052
Log Aggregation Pipeline Broken
Diagnosing silent UDP failures in syslog forwarding
Monitoring
rsyslog
syslog
UDP
Linux
Intermediate

## Slide 2
The Ticket — INCIDENT-MON-003
You arrive cold. This is everything you know.
No logs from app-server-03 in central logging for 48 hours. Rsyslog is installed but forwarding appears broken. Need to fix the log pipeline.
NOT TOLD
What port the aggregator listens on
NOT TOLD
Whether rsyslog is even running
NOT TOLD
What is in the config files
Time to investigate.

## Slide 3
TLDR — In Plain English
Two bugs at the same time, both invisible.
The problem: Logs from this server are supposed to flow to a central collector, but nothing is arriving. UDP makes the failure silent — no errors, no warnings, just missing data.
1
Daemon not running
Rsyslog was configured but never started. The config file exists, but no process is reading it.
2
Wrong port
Config forwards to UDP 5515. The aggregator listens on 5514. One digit off — every packet vanishes.
The fix: Correct the port (5515 → 5514), then start the daemon. Test end-to-end with logger and confirm the message arrives at the aggregator.

## Slide 4
Diagnostic Strategy — Walk the Pipeline
Four stages a log message travels through. Check each in order.
Application
Is something logging?
Rsyslog daemon
Is the forwarder running?
Network
Right port? Right host?
Aggregator
Is it listening and writing?
The natural order:
1. Is the forwarder running at all? (cheapest check — one command) 2. What does the forwarder think it should be doing? (read the config) 3. Is the destination actually listening where the config points? (verify with netstat / ss) 4. Does an end-to-end test message make it through? (the proof)

## Slide 5
Step 1 — Is rsyslog Even Running?
Cheapest diagnostic: ask before reading any config files.
Run this:
$ pgrep rsyslog
What you see: nothing. Empty output, non-zero exit code.
How do I read silence?
No output = no process matching that name. The rsyslog daemon — the thing that reads the config and forwards logs — isn't running. Whatever the config says is irrelevant if there's no process to act on it.
1
BUG #1 FOUND: rsyslog daemon is not running.
Don't start it yet. Verify the config first or you'll fix one bug at a time instead of both.

## Slide 6
Container Quirk — Why service rsyslog status Fails
In a real EC2, you'd use systemctl. In this minimal container, neither works.
What you'll see if you try it:
$ service rsyslog status
rsyslog: unrecognized service
Why?
The container has no systemd. Containers run a single foreground process by design — no init system to manage services. The rsyslog package is installed but never registered an init script in /etc/init.d/, so the service wrapper has nothing to find.
Lab vs Real EC2
Real EC2
systemctl status rsyslog
Modern, with systemd journal integration
Real EC2 (older)
service rsyslog status
SysV / Upstart wrapper
This container
pgrep rsyslog
No init system at all — go direct to processes

## Slide 7
Step 2 — Read the Forwarding Config
Where rsyslog stores custom rules: /etc/rsyslog.d/*.conf drop-ins.
$ cat /etc/rsyslog.d/50-forwarding.conf
# Forward all logs to central aggregation
*.* @127.0.0.1:5515
Reading the line piece by piece
*.*
All facilities, all severities — match every log message
@
Forward over UDP. (Two @@ would mean TCP)
127.0.0.1
Destination host — localhost in this case
:5515
Destination port
Now the question: is port 5515 actually where the aggregator is listening?

## Slide 8
Step 3 — What's Actually Listening?
Trust nothing. Verify what is real, not what the config claims.
$ netstat -ulnp
Active Internet connections (only servers)
Proto Local Address Foreign Address PID/Program
udp 0.0.0.0:5514 0.0.0.0:* 8/python3
udp 127.0.0.11:42981 0.0.0.0:* -
Flag breakdown
-u
UDP only
-l
Listening sockets
-n
Numeric ports
-p
Show process holding socket
2
BUG #2 FOUND
Config says :5515. Aggregator is on :5514. The Python listener (PID 8) tells you the truth.

## Slide 9
Why UDP Fails Silently
The single most important real-world lesson in this lab.
UDP (@)
Connectionless — fire and forget
No handshake, no acknowledgement
Wrong port? Kernel silently drops the packet
No error logged anywhere
You only find out by checking
TCP (@@)
Connection-oriented — handshake required
Wrong port? Connection refused
Rsyslog logs an error you can see
Reliable delivery once connected
Default for production where loss matters
Takeaway: UDP-based pipelines need active verification (does the destination listen? does the test message arrive?). The protocol gives you no error signals.

## Slide 10
Step 4 — Apply Fixes in the Right Order
Config first, then start the daemon. One round of debugging instead of two.
1
Fix the port
$ sed -i 's/5515/5514/' /etc/rsyslog.d/50-forwarding.conf
2
Start the daemon (no systemd, so call binary directly)
$ rsyslogd
Why this order? If you start rsyslog first with the broken config, it confidently forwards messages to a dead end. You've now started a process that's "running but useless" — harder to debug than a stopped one.

## Slide 11
The imklog Warning — Harmless
Expected in unprivileged containers. Does not affect log forwarding.
rsyslogd: imklog: cannot open kernel log (/proc/kmsg):
Operation not permitted.
rsyslogd: activation of module imklog failed
What it means
imklog is rsyslog's kernel log input module. It tries to read the kernel ring buffer at /proc/kmsg, which requires the CAP_SYSLOG capability. Docker containers don't get that capability by default — quite reasonably so.
Why we ignore it
Our test path: logger → local syslog socket → rsyslog → UDP forward → aggregator. imklog is not in that path. The forwarding module loaded fine; we don't need kernel logs.

## Slide 12
Step 5 — Prove the Pipeline Works
Restarting the service is not proof. A test message arriving is.
$ logger -t test "validation check from $(hostname)"
$ sleep 1
$ cat /var/log/aggregated.log
<13>Oct 26 14:32:01 test: validation check from a3f9c2e1b4d7
What just happened
logger
→
/dev/log
→
rsyslog
→
UDP :5514
→
python3
→
/var/log/aggregated.log
If the message appears in the aggregated log, the pipeline is working end-to-end.
Then run: lab validate 052 → 6 of 6 checks should pass.

## Slide 13
Real-World Gotcha Log
Container minimalism vs production EC2 — survival kit, not legacy junk.
Real EC2 (canonical)
This container
Why it differs
systemctl status rsyslog
pgrep rsyslog
No systemd in container
service rsyslog status
pgrep rsyslog
No init script registered
systemctl start rsyslog
rsyslogd (run binary)
Same — no init script
ss -ulnp
netstat -ulnp
iproute2 not installed
(no warning)
imklog: kernel log perm denied
CAP_SYSLOG not granted
The general pattern
Minimal containers, hardened jumphosts, and stripped production servers often lack modern tools. Knowing the older fallbacks is what separates the engineer who ships a fix in 5 minutes from the one stuck SSH'd in not knowing what they have.

## Slide 14
Why This Bug Set Is Realistic
Two simultaneous bugs that mask each other — happens constantly in production.
The story behind incidents like this
1
Someone deploys a new logging config — Terraform module, Ansible playbook, manual SSH session.
2
The deploy writes the config file but the service restart step fails or is skipped.
3
Nobody notices because UDP forwarding to a wrong port produces no errors.
4
Days or weeks later, someone goes looking for logs that should exist and finds nothing.
The masking effect: If only the daemon were down, you'd find the port issue once you started it. If only the port were wrong, you'd find the daemon issue once you saw "no logs". Both broken at once = silence = same symptom = pipeline-walking is the only reliable approach.

## Slide 15
Beyond rsyslog — Production Patterns
The same diagnostic mindset transfers to whatever stack you meet.
ELK / EFK
Rsyslog → Logstash or Fluentd → Elasticsearch → Kibana for search and dashboards.
CloudWatch + Fluent Bit
AWS-native: agent forwards to CloudWatch Logs; query with CloudWatch Insights.
Structured (JSON) logging
Apps emit JSON, not free-text syslog. Forwarder doesn't care; downstream queries are easier.
TLS encryption
@@ with TLS in rsyslog. Logs contain IPs, usernames, stack traces — encrypt in transit.
Disk-assisted queues
Buffer locally if destination is unreachable. Drains when it recovers. Prevents loss during outages.
Firewall / SG rules
A blocked port produces the same symptom as everything else. Always check the network path.
The constant: Walk the pipeline, check each stage, don't trust the config — verify what's actually happening. The diagnostic mindset transfers cleanly across all of these stacks.

## Slide 16
Key Lessons
What to take with you to the next incident.
1
Silent failures are the most dangerous class of bug — UDP gives you zero error signals.
2
Always check the cheapest thing first. "Is the process even running?" takes one command.
3
@ is UDP, @@ is TCP in rsyslog forwarding syntax. Common gotcha — worth memorising.
4
The config tells you what should happen. netstat / ss tells you what is happening. When they disagree, reality wins.
5
logger is your best friend for syslog testing — cleanest way to verify pipelines end-to-end.
6
Walk the pipeline, end to end. Methodically check each stage in order — catches bugs hiding behind other bugs.
7
Know your fallback commands. Minimal containers and hardened hosts often lack modern tools.

## Slide 17
Common Mistakes to Avoid
The traps that turn a 5-minute fix into a 5-hour debugging session.
Starting rsyslog before fixing the config
You now have a process "running but useless" — harder to debug than a stopped one.
Trusting the config without verifying the listener
You'd have started rsyslog and still seen no logs, hunting a different bug.
Panicking at the imklog warning
Red herring in containers. Read the message — kernel log — and ask: do I need that right now?
Using @ (UDP) when destination expects TCP
UDP loses messages silently. Default to TCP unless throughput pressure forces UDP.
Skipping end-to-end tests after the fix
Restarting the service is not proof. A logger message arriving is.
Forgetting firewall / security group rules
In cloud envs, a blocked port looks identical to every other failure. Always check the network path.

## Slide 18
Cleanup & Summary
Disposable container, no AWS resources, no costs.
$ cd ~/cloud-engineer-labs/monitoring-labs/lab-052-log-aggregation-broken
$ docker compose down -v
-v removes anonymous volumes — wipes test logs from this run so the next start is clean. No terraform destroy needed.
To run again from broken state: docker compose up -d. The container rebuilds from the image and re-runs inject-faults.sh — no git checkout needed.
Lab 052 · Difficulty: Intermediate · Category: Monitoring / Logging · Skills: syslog, rsyslog, UDP forwarding, pipeline diagnostics