## Slide 1
Lab 07
Firewall Blocking
Application Ports
iptables • Linux Networking • Security
Cloud Engineer Labs

## Slide 2
The Scenario — What You've Been Handed
Cloud Engineer Labs • Lab 07 — Firewall Blocking
🎫 The Ticket
"App team is reporting that the web application and health check endpoint are unreachable. Deployments look healthy from their side. Can you investigate?"
What do you know at this point?
❓
Is the process running?
You don't know yet
❓
Is it a config issue?
You don't know yet
❓
Is the network/firewall blocking it?
You don't know yet
Your job: work through the layers — systematically.

## Slide 3
Investigative Pathway
Cloud Engineer Labs • Lab 07 — Firewall Blocking
01
Is anything running?
ss -tlnp
Confirm the process is alive and listening on 8080/8081
02
Can you reach it?
curl -s --connect-timeout 2 ...
Prove the block — curl will hang/timeout if firewall is DROP
03
Inspect the firewall
iptables -L INPUT -n --line-numbers
Check the default policy and what rules exist
04
Add rules for 8080 & 8081
iptables -A INPUT -p tcp --dport …
One targeted ACCEPT rule per port — nothing more
05
Verify & test
iptables -L … then curl both ports
Confirm rules are in place, confirm apps respond

## Slide 4
The Fix — Understanding the Command
Cloud Engineer Labs • Lab 07 — Firewall Blocking
iptables -A INPUT -p tcp --dport 8080 -j ACCEPT
-A INPUT
Append a rule to the INPUT chain
(controls all incoming traffic)
-p tcp
Match TCP protocol only
(required before specifying a port)
--dport 8080
Match traffic to destination
port 8080 only
-j ACCEPT
Jump to ACCEPT — let
the packet through
Why not just set the default policy to ACCEPT?
That removes all firewall protection — everything gets through, not just your app ports. You'd be demolishing the fence to open one gate. Always add targeted rules. The DROP default is correct and intentional — work with it, not around it.

## Slide 5
Nobody Uses Raw iptables in Production — So Why Learn It?
Cloud Engineer Labs • Lab 07 — Firewall Blocking
What real engineers use instead
AWS / Cloud
Security Groups — rules sit outside the instance entirely. The host never knows they exist.
Ubuntu / Debian
ufw → ufw allow 8080/tcp
One line. Writes iptables rules under the hood.
RHEL / CentOS
firewalld → firewall-cmd --add-port=8080/tcp
Common in enterprise environments.
So why learn raw iptables?
All of those tools generate iptables rules underneath. When something goes wrong — a Security Group behaves unexpectedly, ufw does something surprising, a Kubernetes network policy blocks traffic — the engineer who can read iptables -L and understand what's actually happening is the one who resolves it.
Everyone else is guessing.
It's the same reason you learn subnetting before you use a CIDR calculator. You may never write raw iptables in production, but you'll understand what every higher-level tool is doing — and why they sometimes get it wrong.

## Slide 6
Key Concepts
Cloud Engineer Labs • Lab 07 — Firewall Blocking
Default DROP = Deny by Default
Nothing gets through unless explicitly permitted. Correct and intentional — don't change it, add rules to it.
Rules are processed top to bottom
First matching rule wins. If nothing matches, the default policy applies.
Process first, firewall second
Always run ss -tlnp before touching iptables. A dead process is a different problem — firewall rules won't fix it.
--connect-timeout is essential
A DROP firewall doesn't send rejection responses — curl hangs forever without a timeout.
One rule per port
Firewalls are explicit. Two services need two rules. No implicit sharing of policies.
-i lo and container networking
Interface scoping works on real servers. Docker strips it silently — omit -i lo in container labs, apply it in real server work.

## Slide 7
Common Mistakes
Cloud Engineer Labs • Lab 07 — Firewall Blocking
✕
Setting default policy to ACCEPT
Removes all firewall protection. You've fixed the symptom by disabling the firewall entirely.
✕
Running iptables -F (flush)
Deletes every rule. Default policy stays DROP. You've locked out everything — including SSH. Catastrophic on a remote server.
✕
Forgetting port 8081
Two services means two rules. Validation checks both. Don't assume one rule covers the whole app.
✕
Skipping ss -tlnp first
If the app has crashed, firewall rules solve nothing. Always confirm the process is alive before touching iptables.

## Slide 8
Lab 07 Complete
The firewall was silently dropping everything.
Two targeted rules. Problem solved. Security intact.
iptables
Default DROP
ACCEPT rules
ss -tlnp
curl --connect-timeout
ufw / Security Groups
Cloud Engineer Labs